## Slide 1: 8086 Instruction Set
Md. Shahidul Salim
Farhan Sadaf

## Slide 2: Arithmetic Instructions
OPCODE | OPERAND | EXPLANATION | EXAMPLE
ADD | D, S | D = D + S | ADD AX, [2050]
SUB | D, S | D = D – S | SUB AX, [SI]
INC | D | D = D + 1 | INC AX
DEC | D | D = D – 1 | DEC [2050]
NEG | D | D = 2’s compliment of D | NEG AL

## Slide 3: Arithmetic Instructions Cont.
OPCODE | OPERAND | EXPLANATION | EXAMPLE
MUL | 8-bit register | AX = AL * 8-bit reg. | MUL BH
MUL | 16-bit register | DX AX = AX * 16-bit reg. | MUL CX
IMUL | 8 or 16 bit register | performs signed multiplication | IMUL CX
DIV | 8-bit register | AX = AX / 8-bit reg. ; AL = quotient ; AH = remainder | DIV BL
DIV | 16-bit register | DX AX / 16-bit reg. ; AX = quotient ; DX = remainder | DIV CX
IDIV | 8 or 16 bit register | performs signed division | IDIV BL

## Slide 4: ADD (Addition)
This instruction adds the data of destination and source operand and stores the result in destination.
Both operands should be of same type i.e. words or bytes otherwise assembler will generate an error.
If the sum of two operands exceeds the size of destination operand, then it would set the carry flag to 1.
The ADD instruction can affect AF, CF, OF, PF, SF, ZF flags depending upon the result. If the result is zero, the ZF=1. Negative result sets SF to 1.
Source | Destination | Example
Register | Register | ADD AX, BX
Register | Immediate | ADD CL, 2DH
Register | Memory Address | ADD [204CH], AL ADD [BP][SI]+23, DX
Memory Address | Register | ADD CL, [BX+15]

## Slide 5: ADD (Example) Cont.
ORG 100h ;This directive required for a simple 1 segment .com program
MOV AL, 10H ;Sets AL to 10H
MOV BH, 75H ;Sets BX to 23H
ADD AL, BH ;Store the sum of AL and BX in AL
MOV CX, 0F21Ah ;Set CX to 0F21Ah
ADD [0154H], CX ;Store sum of CX and data at memory address DS:0154 in DS:0154
RET ;stops the program

## Slide 6: SUB (Subtraction without Carry)
Subtract the data in the source operand from the data of destination operand and then store the result back to the destination operand.
Just like ADD instruction, both operands should be either in bytes or words.
The SUB instruction can affect AF, CF, OF, PF, SF and ZE flags depending upon the result obtained from difference.
Source | Destination | Example
Register | Register | SUB CH, AL
Register | Immediate | SUB AX, 16H
Register | Memory Address | SUB [SI], AX SUB 19[BP][DI], CX
Memory Address | Register | SUB AL, 10[CX]

## Slide 7: SUB (Example) Cont.
ORG 100h
MOV AX, 2506 ;Sets AX to 2506
MOV BX, 1647 ;Sets BX to 1647
SUB AX, BX ;AX = AX - BX
SUB [SI], AX ;DS:SI = DS:SI - AX
RET ;stops the program

## Slide 8: INC (Increment)
Takes only one operand.
Adds 1 to the contents of destination operand.
ORG 100h
MOV AL, 7DH ;Sets AL to 7DH
INC AL ;AL = AL+1
RET ;stops the program

## Slide 9: DEC (Decrement)
Subtracts 1 from the destination operand and loads the result back into the same destination.
ORG 100h
MOV AL, 7DH ;Sets AL to 7DH
DEC AL ;AL = AL-1
RET ;stops the program

## Slide 10: MUL (Unsigned Multiplication)
Handles unsigned data.
There are types of multiplication depending on the number of bits:
  Byte with byte
  Word with Word
  Byte with word
OPCODE | OPERAND | EXPLANATION | EXAMPLE
MUL | 8-bit register | AX = AL * 8-bit reg. | MUL BH
MUL | 16-bit register | DX AX = AX * 16-bit reg. | MUL CX

## Slide 11: MUL (Example) Cont.
MOV AL, 5H ;a byte is moved to AL
MOV BL, 10H ;immediate data must be in BL register
MUL BL ;AX = 0050h, CF = 0
8-Bit Multiplication
MOV AX, 2000H ;a word is moved to AX
MOV BX, 0100H ;immediate data must be in BX register
MUL BX ;DX:AX = 00200000H, CF = 1
16-Bit Multiplication
The Carry flag is set because the upper part of the product (located in DX) is not equal to zero.

## Slide 12: IMUL (Signed Multiplication)
Handles signed data operands meaning the operands can be positive or negative.
When the operand is a byte, it is multiplied with AL register.
When the operand is a word, it is multiplied with AX register.
If the product of multiplier and multiplicand produce result that fits into the destination register DX and AX with some of the bits left unused. Then these unused bits are filled with the copies of signed bit and clear CF and OF flags to zero.
OPCODE | OPERAND | EXPLANATION | EXAMPLE
IMUL | 8 or 16 bit register | performs signed multiplication | IMUL CX

## Slide 13: IMUL (Example) Cont.
MOV AL, -4 ;a byte is moved to AL
MOV BL, 4 ;immediate data must be in BL register
IMUL BL ;AX = FFF0H, OF = 0
The following instructions multiply 4 by 4, producing (-16) in AX.
AH is a sign extension of AL so the Overflow flag is clear.

## Slide 14: DIV (Unsigned Division)
In the expression a ÷ b = c,
  a is called the dividend or numerator,
  b the divisor or denominator
  and the result c is called the quotient.
DIV instruction performs the division of two unsigned operands.
The divisor resides in a source operand and it should not be immediate. However, it can be register or a memory location.
There are four division cases depending on the number of bits:
  Byte with byte
  Word with word
  Word with byte
  Doubleword with word

## Slide 15: DIV (Unsigned Division) Cont.
OPCODE | OPERAND | EXPLANATION | EXAMPLE
DIV | 8-bit register | AX = AX / 8-bit reg. ; AL = quotient ; AH = remainder | DIV BL
DIV | 16-bit register | DX AX / 16-bit reg. ; AX = quotient ; DX = remainder | DIV CX

## Slide 16: DIV (Example) Cont.
ORG 100h
.DATA
NUM_1 DB 0F2H
NUM_2 DB 4H
.CODE
MOV BH, NUM_2 ;Load numerator in BH
MOV AL, NUM_1 ;Load denominator in AL
DIV BH ;Divide BH by AL
RET
Byte with Byte Division
In this case, the nominator and denominator operands are bytes.
The nominator resides in the AL register and AH is set to zero.
After division, the instruction stores quotient in AL and the remainder in AH register.

## Slide 17: DIV (Example) Cont.
ORG 100h
.DATA
NUM_1 DW 0F213H
NUM_2 DW 41A8H
.CODE
MOV AX, NUM_1 ;Load numerator in AX
DIV NUM_2 ;Divide AX by NUM_2
RET
Word with Word Division
In this case, the AX register holds the numerator.
After division, the quotient is stored in the AX register and the remainder goes to the DX register.

## Slide 18: DIV (Example) Cont.
ORG 100h
.DATA
NUM_1 DW 1B25H
NUM_2 DB 24H
.CODE
MOV AX, NUM_1 ;Load denominator in AX
DIV NUM_2 ;Divide AX by NUM_2
RET
Word with Byte Division
The numerator is a 16-bit word stored in AX which is divided with an 8-bit denominator.
After division, the AL contains the quotient and AH will contain the remainder.

## Slide 19: DIV (Example) Cont.
ORG 100h
.DATA
NUM_1 DW 2413H
.CODE
MOV AX, 5670 ;Load lower bytes of numerator in AX
MOV DX,4531 ;Load highe bytes of numerator in DX
DIV NUM_1 ;Divide AX by NUM_1
RET
Double word with Byte Division
Numerator is a 32-bit number and a denominator is a 16-bit number.
In this case, AX and DX stores the numerator. The most significant part resides in the DX register and the least significant bits of numerator are in the AX register.
After the execution of DIV instruction, the remainder goes to DX register and the quotient lie in AX register.

## Slide 20: IDIV (Signed Division)
Performs a division operation between two signed numbers.
Just like DIV instruction, the IDIV instruction also has four cases.
ORG 100h
.DATA
NUM_1 DD 0C250A91H
NUM_2 DW -0B25H
NUM_3 DB 24H
.CODE
;Byte by Byte Signed Division
MOV AL, NUM_3
MOV BL,3
IDIV BL
;Word by word Signed Division
MOV AX, -265H
IDIV NUM_2
;Word by byte Signed Division
MOV AX, NUM_2
IDIV NUM_3
;Doubleword by single word signed division
MOV AX,NUM_1
MOV DX, NUM_1+2
MOV BX, 0A234H
IDIV BX
RET

## Slide 21: Logical Instructions
OPCODE | OPERAND | EXPLANATION | EXAMPLE
AND | D, S | D = D AND S | AND AX, 0010
OR | D, S | D = D OR S | OR AX, BX
NOT | D | D = NOT of D | NOT AL
XOR | D, S | D = D XOR S | XOR AL, BL
SHR | D, C | shifts each bit in D to the right C times and 0 is stored at MSB position | SHR AL, 04
SHL | D, C | shifts each bit in D to the left C times and 0 is stored at LSB position | SHL AX, BL

## Slide 22: Logical Instructions Cont.
OPCODE | OPERAND | EXPLANATION | EXAMPLE
ROR | D, C | rotates all bits in D to the right C times | ROR BL, CL
ROL | R, C | rotates all bits in D to the left C times | ROL BX, 06
RCR | D, C | rotates all bits in D to the right along with carry flag C times | RCR BL, CL
RCL | R, C | rotates all bits in D to the left along with carry flag C times | RCL BX, 06

## Slide 23: CMP (Comparison Instruction)
CMP is a logical instruction which compares a byte or word in the destination with a byte or word in the specified source.
The destination can be a register or a memory location but the source and the destination cannot both be memory locations.
This instruction will not affect the source and destination, only the flags (AF, OF, SF, ZF, PF, and CF) are set to indicate the results of the comparison.
      Instruction Operands
      ---------------------------------------
        CMP REG, memory
        memory, REG
        REG, REG
        memory, immediate
        REG, immediate

## Slide 24: CMP (Example) Cont.
CMP CX, BX ; CX-BX
CF ZF SF
CX = BX 0 1 0 Result of subtraction is 0
CX > BX 0 0 0 No borrow required, so CF = 0
CX < BX 1 0 1 Subtraction requires borrow, so CF = 1

## Slide 25: Unconditional Program execution
OPCODE | OPERAND | EXPLANATION
CALL | address | Used to call a procedure and save their return address to the stack.
RET | ---- | Used to return from the procedure to the main program.
JMP | address | Used to jump to the provided address to proceed to the next instruction.
LOOP | address | Used to loop a group of instructions until the condition satisfies, i.e., CX = 0

## Slide 26: Conditional Program execution
OPCODE | OPERAND | EXPLANATION
JC | address | Used to jump if carry flag CY = 1
JNC | address | Used to jump if no carry flag (CY = 0)
JE/JZ | address | Used to jump if equal/zero flag ZF = 1
JNE/JNZ | address | Used to jump if not equal/zero flag ZF = 0
JO | address | Used to jump if overflow flag OF = 1

## Slide 27: Conditional Program execution Cont.
OPCODE | OPERAND | EXPLANATION
JNO | address | Used to jump if no overflow flag OF = 0
JC | address | Used to jump if carry flag CY = 1
JCXZ | address | Used to jump to the provided address if CX = 0
LOOPE/ LOOPZ | address | Used to loop a group of instructions till it satisfies ZF = 1 & CX = 0

## Slide 28: References
https://www.geeksforgeeks.org/arithmetic-instructions-8086-microprocessor/
https://microcontrollerslab.com/8086-integer-arithmetic-instructions-assembly-language-programming/
https://microdigisoft.com/8086-integer-multiplication-instructions/#8-bit-multiplication
https://microcontrollerslab.com/8086-integer-division-instructions-assembly-programming/
https://www.geeksforgeeks.org/logical-instructions-8086-microprocessor/
https://4beginner.com/8086-CMP-Instruction#:~:text=8086%20CMP%20Instruction%20Edit&text=CMP%20is%20a%20logical%20instruction,cannot%20both%20be%20memory%20locations.
https://www.tutorialspoint.com/program-execution-transfer-instructions-in-8086-microprocessor